## Slide 1: Estimote & Disk Distance Test

## Slide 2: Research Purpose
For this test I will be conducting multiple tests with both Estimote and Disk beacons in various distances up to 3 meters and with the beacons in different positions such as on the roof and on the side of walls at different heights. The beacons will all best up at standard Interval periods of 100ms. The test will run for max time of 90 seconds and the Phone will be mounted on a try pod for a constant height and position of the device facing the beacons camera facing. I will also be using the same beacons for this test of consistence and will run the tests 4 times and work out the averages from there and for a better idea of consistence of the tests.
Beacon | Estimote | Disk
RSSI | -20 dBm | -23 dBm
Interval period | 100ms | 100ms

## Slide 3: Beacons standing upright
For this test I will be placing the beacons on the white board with the distance of 0.50 meters above the scanning area (desk) and will be having the phone attached to the tripod and each distance will have four test run to try and work out an average RSSI power reading for both the Estimote and Disk beacon. The test scan will be set to run for 90 seconds, the beacons will not be changed out at any point during this test.

## Slide 4: 1cm Scan
Test Details:
The distance from the desk and the beacon is 0.5 meters and this will be kept constant throughout the tests.
The hypotenuse of the triangle of is worked out using standard trigonometry and is equal to 0.50.
0.01 meters = 1cm is the measurement from the wall to the phone and this will be alternating measurement.
Beacons
Desk
0.5m
0.5m
0.01m
iPhone

## Slide 5
1cm Disk vs Estimote

## Slide 6: 10cm Scan
Test Details:
The distance from the desk and the beacon is 0.5 meters and this will be kept constant throughout the tests.
The hypotenuse of the triangle of is worked out using standard trigonometry and is equal to 0.51.
0.10 meters = 10cm is the measurement from the wall to the phone and this will be alternating measurement.
Beacons
Desk
0.51m
0.5m
0.10m
iPhone

## Slide 7
10cm Disk vs Estimote

## Slide 8: 20cm Scan
Test Details:
The distance from the desk and the beacon is 0.5 meters and this will be kept constant throughout the tests.
The hypotenuse of the triangle of is worked out using standard trigonometry and is equal to 0.54.
0.20 meters = 20cm is the measurement from the wall to the phone and this will be alternating measurement.
Beacons
Desk
0.54m
0.5m
0.20m
iPhone

## Slide 9
20cm Disk vs Estimote

## Slide 10: 30cm Scan
Test Details:
The distance from the desk and the beacon is 0.5 meters and this will be kept constant throughout the tests.
The hypotenuse of the triangle of is worked out using standard trigonometry and is equal to 0.58.
0.30 meters = 30cm is the measurement from the wall to the phone and this will be alternating measurement.
Beacons
Desk
0.54m
0.5m
0.30m
iPhone

## Slide 11
30cm Disk vs Estimote

## Slide 12: 40cm Scan
Test Details:
The distance from the desk and the beacon is 0.5 meters and this will be kept constant throughout the tests.
The hypotenuse of the triangle of is worked out using standard trigonometry and is equal to 0.64.
0.40 meters = 40cm is the measurement from the wall to the phone and this will be alternating measurement.
Beacons
Desk
0.64m
0.5m
0.40m
iPhone

## Slide 13
40cm Disk vs Estimote

## Slide 14: 50cm Scan
Test Details:
The distance from the desk and the beacon is 0.5 meters and this will be kept constant throughout the tests.
The hypotenuse of the triangle of is worked out using standard trigonometry and is equal to 0.71.
0.50 meters = 50cm is the measurement from the wall to the phone and this will be alternating measurement.
Beacons
Desk
0.71m
0.5m
0.50m
iPhone

## Slide 15
50cm Disk vs Estimote

## Slide 16: 1m Scan
Test Details:
The distance from the desk and the beacon is 0.5 meters and this will be kept constant throughout the tests.
The hypotenuse of the triangle of is worked out using standard trigonometry and is equal to 1.12m.
1.0 meters = 100cm is the measurement from the wall to the phone and this will be alternating measurement.
Beacons
Desk
1.12m
0.5m
1m
iPhone

## Slide 17
1m Disk vs Estimote

## Slide 18: 2m Scan
Test Details:
The distance from the desk and the beacon is 0.5 meters and this will be kept constant throughout the tests.
The hypotenuse of the triangle of is worked out using standard trigonometry and is equal to 2.06m.
2.0 meters = 200cm is the measurement from the wall to the phone and this will be alternating measurement.
Beacons
Desk
2.06m
0.5m
2m
iPhone

## Slide 19
2m Disk vs Estimote

## Slide 20: 3m Scan
Test Details:
The distance from the desk and the beacon is 0.5 meters and this will be kept constant throughout the tests.
The hypotenuse of the triangle of is worked out using standard trigonometry and is equal to 3.04m.
3.0 meters = 300cm is the measurement from the wall to the phone and this will be alternating measurement.
Beacons
Desk
3.03m
0.5m
3m
iPhone

## Slide 21
3m Disk vs Estimote

## Slide 22: Overview

## Slide 23
Over all beacon scans
Chart: All Beacon Scans
| 1cm | 10cm | 20cm | 30cm | 40cm | 50cm | 1m | 2m | 3m
Estimote | -83 | -80 | -85 | -81 | -84 | -81 | -76 | -86 | -85
Disk | -75 | -73 | -81 | -78 | -75 | -80 | -80 | -79 | -84
Difference | -8 | -7 | -4 | -3 | -9 | -1 | 4 | -7 | -1

## Slide 24
Distance | Estimote | Disk | Difference
1cm | -83 | -75 | -8
10cm | -80 | -73 | -7
20cm | -85 | -81 | -4
30cm | -81 | -78 | -3
40cm | -84 | -75 | -9
50cm | -81 | -80 | -1
1m | -76 | -80 | 4
2m | -86 | -79 | -7
3m | -85 | -84 | -1
Averages of all 4 tests